## Slide 1: Lab 1: Arduino Basics
Topics: Arduino Fundamentals, First Circuit
Date: Aug 26, 2016

## Slide 2: References (study these)
https://www.arduino.cc/en/Guide/Introduction
https://www.arduino.cc/en/Tutorial/Foundations
https://www.arduino.cc/en/Guide/BoardAnatomy
https://www.arduino.cc/en/Tutorial/DigitalPins
https://www.arduino.cc/en/Tutorial/AnalogInputPins
https://www.arduino.cc/en/Tutorial/PWM
https://www.arduino.cc/en/Tutorial/Memory
https://www.arduino.cc/en/Reference/PinMode
https://www.arduino.cc/en/Reference/DigitalWrite
https://www.arduino.cc/en/Reference/DigitalRead
https://www.arduino.cc/en/Reference/AnalogRead
https://www.arduino.cc/en/Reference/AnalogWrite
https://www.arduino.cc/en/ArduinoStarterKit/Prj02

## Slide 3: What is Arduino?
“Open-source prototyping platform based on easy to use HW and SW.”
  Inexpensive
  Cross-platform
  Simple programming environment (IDE)
  Open-source SW and HW

## Slide 4: Making Stuffs using Arduino
You can connect sensors and actuators, and program your Arduino to control them.
Actuators (output)
Sensors (input)

## Slide 5: Arduino Uno Anatomy
http://arduinoarts.com/tag/anatomy/

## Slide 6: Know Your Tools
(all images are from Google image search)

## Slide 7: Program Structure
setup() – executed once at the beginning.
loop() – it’s an infinite loop.

## Slide 8: Arduino Language Reference
Almost the same as C with some new things:
  setup() and loop()
  Constants: HIGH, LOW, INPUT, OUTPUT
  PROGMEM, EEPROM
  Digital/Analog input/output functions
  Library methods for – character, bits, interrupts, and communication.
https://www.arduino.cc/en/Reference/HomePage

## Slide 9: Digital Read and Write
Digital IO: HIGH or LOW
int ledPin = 13; // LED connected to digital pin 13
int inPin = 7; // pushbutton connected to digital pin 7
int val = 0; // variable to store the read value
void setup()
{
pinMode(inPin, INPUT); // sets digital pin 7 as input
pinMode(ledPin, OUTPUT); // sets digital pin 13 as output
}
void loop()
{
val = digitalRead(inPin); // read the input pin (button)
digitalWrite(ledPin, val); // sets the LED to the value
}

## Slide 10: Analog Read
Arduino UNO has a 10-bit analog-to-digital converter, so input voltage mapped to [0, 1023]
int analogPin = 3;
// potentiometer middle terminal connected to analog pin 3 outside leads to ground and +5V
int val = 0; // variable to store the value read
void setup()
{
Serial.begin(9600); // setup serial
}
void loop()
{
val = analogRead(analogPin); // read the input pin
Serial.println(val); // debug value
}

## Slide 11: Analog Write (PWM)
Getting analog results with digital means.
Must be [0, 255], and it will mean “duty cycle”.
pinMode(9, OUTPUT);
int X = 123;
analogWrite(9, X);

## Slide 12: Memory
TYPE | SIZE (UNO) | USE | Volatile?
Flash | 32K | Program space | No
SRAM | 2K | Variables | Yes
EEPROM | 1K | Long term information | No
Optimizing SRAM use:
  Use a connected smartphone/computer to move data out for calculation.
  Use smaller data types (byte if you don’t need an int.)
  Use Flash memory (PROGMEM keyword)
  Use EEPROM (use EEPROM library)

## Slide 13: Variety of Arduino Boards

## Slide 14: Expanding Arduino with ‘Shields’
Arduino + GPS Shield
Arduino + Joy Stick Shield
Arduino + Xbee Shield

## Slide 15: Lab Work: “Spaceship Interface”
It’s project #2 of Arduino Projects Book.
https://www.arduino.cc/en/ArduinoStarterKit/Prj02
Once you are done, please take an extra 5 minutes to put all electronic elements back into the box.